## Slide 1
RFID Badge Cloning and Protection Mechanisms
Created by Reem hany Abd El raouf 20236039,
Marwan ossama Hussein 20235035,
Moaz Mohamed salah 20236063.

## Slide 2
Introduction to RFID Technology
What is RFID Technology?
Radio-Frequency Identification (RFID) technology uses electromagnetic fields to automatically identify and track tags attached to objects. It enables contactless communication between a tag and a reader, facilitating various applications across industries.
Ubiquitous Applications
Supply Chain
Streamlining inventory tracking and logistics
Access Control
Facilitating secure building and system access
Payment Systems
Enabling secure and convenient transactions
Security Challenges
Badge Cloning Vulnerability
While offering convenience, RFID systems face significant security challenges. The widespread adoption introduces inherent vulnerabilities, particularly concerning badge cloning, where unauthorized duplicates can be created to bypass security measures.
RFID Badge Cloning and Protection Mechanisms

## Slide 3
Core Components of RFID Systems
RFID Tag interacting with Reader
RFID Tag (Badge)
Small microchip attached to an antenna
Stores data, including unique identifier
Transmits data when activated
Can be passive or active (self-powered)
RFID Reader
Emits radio waves to activate tags
Reads data from tags
Converts radio waves to digital data
Sends data to host computer
Back-End System
Server and database infrastructure
Application software for processing
Receives and processes tag data
Performs actions (access, tracking, payment)
Working together: These three components form an integrated system that enables wireless identification and data exchange. When a tag enters the reader's field, it responds with its stored data, which the reader converts and sends to the back-end system for processing and action.
RFID Badge Cloning and Protection Mechanisms

## Slide 4
RFID Operating Frequencies
RFID systems operate across various frequency bands, each with distinct characteristics influencing their application in access control systems.
Low Frequency (LF)
125-134 kHz
Characteristics:
Short read range (few centimeters)
Slower data transfer rates
Less susceptible to interference from liquids or metals
Applications:
Basic access control
Simple building access systems
Common cards: EM4100
High Frequency (HF)
13.56 MHz
Characteristics:
Moderate read range (up to a meter)
Faster data transfer speeds
More data storage capacity
Applications:
Enhanced security access
Requires more data storage and security
Common cards: Mifare Classic, DESFire EV1/EV2
RFID Badge Cloning and Protection Mechanisms

## Slide 5
The Threat: RFID Badge Cloning
What is Badge Cloning?
RFID badge cloning involves creating an unauthorized duplicate of an existing RFID access credential, allowing an attacker to bypass physical security measures.
Why It Matters
Requires minimal technical expertise
Uses readily available, inexpensive tools
Difficult to detect without specialized monitoring
Security Implications
Cloned badges can be used to gain unauthorized access to secure facilities, bypassing physical security measures and potentially causing significant damage to an organization's operations and reputation.
Flipper Zero device being used to interact with an access card reader
How Cloning Bypasses Security
Read UID: Attacker reads the static UID from a legitimate badge
Copy Data: Extracts and stores the UID and other data
Create Duplicate: Writes the copied data to a blank card
RFID Badge Cloning and Protection Mechanisms

## Slide 6
Badge Cloning Process
Step 1: Covert Reading
Attackers use specialized RFID readers, often disguised or concealed, to scan legitimate badges when they're in close proximity.
Step 2: Copy UID
The device extracts the unique identifier (UID) and other unencrypted data stored on the tag.
Step 3: Write to Blank
The extracted UID and data are written onto blank, writable RFID cards. These blank cards are inexpensive and widely available.
Key Insight
The simplicity of this process, combined with the accessibility of tools and blank cards, makes RFID badge cloning a significant security concern. Attackers can often complete the process with minimal technical expertise and readily available tools.
RFID Badge Cloning and Protection Mechanisms

## Slide 7
Tools Used for Cloning
Attackers utilize a range of hardware and software tools for RFID badge cloning, many of which are accessible and relatively low-cost, contributing to the widespread nature of this threat.
Proxmark3
Open-source RFID research tool
Reads, writes, and sniffs tags
Operates across LF and HF frequencies
Flipper Zero
Multi-tool device for pentesters
RFID and NFC capabilities
Reads, emulates, and writes tags
Mobile Apps
Smartphones with NFC readers
Limited to HF frequencies
Common phone becomes cloning tool
Key Insight: The accessibility and relatively low cost of these tools contribute to the widespread nature of RFID badge cloning as a security threat.
RFID Badge Cloning and Protection Mechanisms

## Slide 8
Vulnerable RFID Systems
Static UID Vulnerability
Systems that rely solely on the static Unique Identifier (UID) of an RFID card are highly susceptible to cloning attacks. This vulnerability stems from the fact that the UID is often transmitted in plain text and does not change, making it easy to intercept and duplicate.
EM4100
Low Frequency (125 kHz)
Among the simplest and most widely used for basic access control
Transmit a fixed, unencrypted UID
Extremely easy to clone with basic LF readers and writers
Mifare Classic
High Frequency (13.56 MHz)
More complex than EM4100 but still vulnerable
Known cryptographic vulnerabilities allow UID and sector data to be read
Many older access control systems still utilize these cards
Despite their vulnerabilities, these card technologies remain widely deployed due to their simplicity, cost-effectiveness, and perceived adequacy for basic access control needs.
RFID Badge Cloning and Protection Mechanisms

## Slide 9
Protection Mechanisms: Encryption and Authentication
Strengthening RFID Security
Secure RFID systems implement cryptographic techniques and authentication protocols to prevent unauthorized access and cloning.
Dynamic Authentication
Challenge-Response Authentication
The reader issues a unique challenge to the card, which responds with a cryptographically generated answer, preventing simple replay attacks.
Advanced Security Solutions
NXP DESFire EV1/EV2
Implements AES encryption and mutual authentication, providing strong protection against cloning.
Security Comparison
Vulnerable Systems
• Static UIDs
• Plain text transmission
• No encryption
Secure Systems
• Dynamic authentication
• Encrypted communication
• Mutual verification
RFID Badge Cloning and Protection Mechanisms

## Slide 10
Multi-Factor Authentication
Enhanced Security through Multiple Verification Methods
Multi-Factor Authentication (MFA) significantly enhances physical access control security by requiring users to present two or more distinct forms of verification before granting access.
Benefits of MFA
Even if one factor is compromised, access remains protected
Significantly increases difficulty for unauthorized access
Verifies user identity through multiple verification methods
RFID + PIN Code
User must present badge and enter PIN
RFID + Biometrics
Badge with fingerprint/iris scan verification
RFID + Mobile
Badge with mobile code or approval
Dual Card
Two badges for sensitive areas
WAVE ID® Bio Reader
RFID Badge Cloning and Protection Mechanisms

## Slide 11
System-Level Defenses
Beyond individual card and reader security, robust system-level defenses are essential for a comprehensive security posture. These measures are implemented on the back-end access control system to detect and prevent anomalous activities.
Anomaly Detection
Monitors access patterns for unusual behavior, such as a single badge being used at geographically impossible locations within a short timeframe.
Anti-Passback Rules
Prevents badge misuse by ensuring a user cannot pass their badge back to another person. Can be implemented as hard (blocking re-entry) or soft (logging violations).
Time-Based Restrictions
Limits badge access to specific times or days, ensuring that even if a badge is cloned, its utility is restricted to authorized periods.
Regular Security Audits
Periodic reviews of access control system logs, configurations, and physical security measures to identify vulnerabilities and ensure compliance.
Video Surveillance Integration
Links access events with video footage allows for visual verification of individuals using badges, helping to identify unauthorized use.
Comprehensive Protection
System-level defenses provide layered security that complements card-level protections, creating a defense-in-depth approach to RFID security.
RFID Badge Cloning and Protection Mechanisms

## Slide 12
Conclusion
Key Takeaways
1 - RFID technology offers undeniable convenience, but this comes with inherent security vulnerabilities, particularly the risk of badge cloning. Effective security against such threats necessitates a layered defense strategy rather than reliance on a single protective measure.
Continuous awareness and proactive implementation of security protocols are paramount
.
RFID Badge Cloning and Protection Mechanisms
2 - Provide Security Awareness Training
Educate employees on the importance of protecting their RFID badges. Training should cover topics such as not lending badges, reporting lost or stolen badges immediately, and being wary of suspicious individuals attempting to read badges covertly

## Slide 13
RFID Badge Cloning Detector demo
.
RFID Badge Cloning and Protection Mechanisms

## Slide 14
Right Panel — Authorized Badges
.
RFID Badge Cloning and Protection Mechanisms
What is 'Authorized Badges'?
• This is the demo's 'database' of trusted badges kept in the browser (localStorage).
• Each entry: { uid: 'HEX', owner: 'Name' } — UID is the key, owner is the expected presenter.
Entries shown in screenshot:
• Alaa — UID: 04A3B21F (Simulate Clone)
- Means: if a card reads UID 04A3B21F and name 'Alaa' →
Genuine.
- Simulate Clone button: inserts a fake usage of the same UID with a different owner to show detection.
• Hossam — UID: 77F91C02 (Simulate Clone)
• Mona — UID: 9B12D4E8 (Simulate Clone)
Note: localStorage persists per browser — other users/machines won't see these entries

## Slide 15
Left Column — Inputs & Controls
.
RFID Badge Cloning and Protection Mechanisms
Card UID (hex) — Purpose & Details
• Purpose: uniquely identifies an RFID badge (presented as hex).
• Why needed: server-free identity check — UID is the primary key.
• Validation in demo: normalized to uppercase and trimmed; no cryptographic checks.
Presented owner name — Purpose & Details
• Purpose: captures the person claiming to present the card.
• Why needed: allows detection of mismatches when same UID used by different person.
• Limitation: name is free-text; can be easily spoofed.
Buttons — What they do (UX -> code)
• Scan — triggers detect(uid, owner) and recordResult(...). Clears inputs after scanning.
• Register UID — adds (uid, owner) to Authorized Badges (localStorage).
• Reset Data — clears localStorage (authorized list + history).
• Example (Genuine) — fills inputs with a registered UID and matching owner.
• Example (Clone) — fills inputs with a registered UID but different owner to show cloning.

## Slide 16
Simulate Clone — Purpose & Behavior
.
RFID Badge Cloning and Protection Mechanisms
• What simulate clone does:
• It creates an entry in Scan History where the same UID is used by a different owner (e.g., 'FakeUser').
• Shows the UI result 'Clone Detected' and a red status pill — illustrates detection logic without needing a real cloned card.
Why it's useful:
• Educational: demonstrates the exact mismatch condition the system uses to flag cloning.
• Reproducible: instructors can reproduce the cloning case during demos.
Limitation:
• It's a simulated event — real cloning might involve replay attacks, sector/key cloning, or different UID strategies.

## Slide 17
Scan History & Result
.
RFID Badge Cloning and Protection Mechanisms
Scan History
• Shows a timestamped list of recent scans (status, uid, owner, reason).
• Implemented by recordResult() which pushes to an array and saves to localStorage.
• Useful for audit and forensic demonstration in class; limited retention (keeps last 200 entries).
Result Box
• Shows the immediate result of a scan: status pill (Genuine/Clone/Unknown) and a short reason.
• Visual cues: green-ish for Genuine, red for Clone Detected, yellow for Unknown.
• Implemented by showResult() which sets text and styles.

## Slide 18
Limitations, Security Notes & Extensions
.
RFID Badge Cloning and Protection Mechanisms
Limitations
• UID as sole identifier is weak: many real systems use cryptographic authentication or unique keys per sector.
• localStorage is not secure or shared across machines—suitable for demos only.
• Name field is free-text and can be spoofed; real systems use additional verification (PINs, biometrics).
Possible extensions
• Server-side logging + central authorized DB for audit and revocation.
• Use challenge-response or cryptographic tokens instead of plain UID.
• Add rate-limiting, alerting, and locking for repeated clone attempts

## Slide 19
.
RFID Badge Cloning and Protection Mechanisms
THANK YOU